## Slide 1: Dark Wolf Hack Our Drone
Introduction

## Slide 2: Our UAS: Uncrewed Aerial Vehicle
Ready to Sky 250mm FPV
  NEO-6M GPS
  12A ESC BLHELI 14.2 Firmware
  1806 Motors
  Generic “dumb” Power Distribution
  2SP1 7.4V 2200mAh 100C LiPo
BeagleBone Blue Flight Computer
  Debian 10 IoT
  AM335x 1GHz ARM Cortex-A8 processor 512MB DDR3 RAM
  RTU

## Slide 3: Beagle Bone Blue: Flight Computer

## Slide 4: Our UAS: Ground Control System
Wuzcon Game Controller
  PS4 Dual Shock Clone
  Wired Joystick Input
Huawei Nexus 6P
  Android 8.1.0

## Slide 5: A Few Words About Security Testing

## Slide 6: Threat Modeling
Generic Risk Model with Key Risk Factors (NIST SP 800-30 R1)
https://wentzwu.com/2019/08/26/the-nist-generic-risk-model/

## Slide 7: Intro: Cyber Kill Chain
Cyber Kill Chain
Attacks involve a series of tasks
Understanding those tasks help defenders anticipate and harden vulnerable systems
Understanding those tasks help testers to evaluate risk associated with enumerated vulnerabilities

## Slide 8: System Decomposition and Interfaces
Hardware
  UAV
  GCS
  Telemetry Radio
  RC Radio
  Payload
Software
  Flight Software / Firmware
  Supply Chain
  Software Libraries
Sensors
  GPS
  ADS-B
  DroneID
Services
  Cloud
Software Libraries
Supply Chain
RF
RF
Wifi
Wifi
GPS
ADS-B

## Slide 9: Work Shop

## Slide 10: Ground Rules
UAV: Don’t power from two sources
You can power from Micro USB interface on the front of the BeagleBone
If you power from the LiPo, be very careful with the direction of the plugs
You can short the Battery Input on the board
GCS:
To connect to the ArduPilot flight software
Connect to the WiFi that matches your UAV
Set a static IP address of 192.168.8.150 on the phone Modules: Aiming for 30 minutes for each module
Work in pairs
Kali Linux or Windows

## Slide 11: Workshop Lab Modules
Module 1: Ground Control System
  Task 1: Extract Files
  Task 2: Analyze Firmware
  Task 3: Identify WiFi Password
Module 2: Unmanned Aerial Vehicle
  Task 1: Access the UAV
  Task 2: Escalate Privilege
  Task 3: Root and Loot
Module 3: Communications
  Task 1: Collect 802.11 traffic
  Task 2: Crack WiFi password
  Task 3: Monitor MAVLink Traffic